## Slide 1: High Amplitude Modulation of the Magnetic Field at RF Frequency
Roy Elbaz, Yaakov Yudkin, Lev Khaykovich
Bar-Ilan University

## Slide 2
Motivation

## Slide 3
Motivation
RF pulses are often used for molecule production in cold-atoms experiments.

## Slide 4
Motivation

## Slide 5
BEC (Rb)
Degenerate Fermi gas (K)
Rb
K
Rb
K
Adiabatically changing the magnetic field
“STIRAP”

## Slide 6
BEC (Rb)
Degenerate Fermi gas (K)
Conversion efficiency of % for thermal gas
“STIRAP”
“STIRAP” process has >90% efficiency

## Slide 7
So where is the problem?
Wanted attributes:
Large conversion efficiency.
Short coupling time (compared to life-time).
Short coupling time  High modulation amplitude is needed  High current (@ high frequency).
Difficult to accomplish due to the antenna inductance.

## Slide 8
Solution
We added a capacitor and then the RF antenna is the inductor of an LC circuit.
This causes a resonant behavior  all the current that can be provided by the source (VCC) is provided.
The result - our system enables us to carry out magnetic RF pulses with a high current of , and a pulse duration of .
Limitation - discrete values for the frequency.
We overcome this by varying our DC magnetic field.

## Slide 9
Our system is composed out of the following elements:
  Power supplier (VCC).
  Arbitrary function generator (input signal).
  Signal amplifier (RF MOSFET driver).
  LC circuit (including the RF magnetic pulse generator).
Signal Amplifier
VCC
Input
System Description
Atoms
C

## Slide 11
VCC provides a constant voltage of 15V (can provide up to 10A).
Signal Apmlifier
VCC
Input
System Operation
Atoms
A function generator provides a square wave signal @ ~10MHz.
A MOSFET driver connects the VCC to the output according to the input signal.
C
15V
The LC circuit filters out all frequencies but the resonance frequency.
A high current sine wave is provided to the antenna.

## Slide 12
MOSFET Driver Full Circuit

## Slide 13
MOSFET Driver Full Circuit
10μF (Tantalum) capacitors for protecting the circuit from rapid spikes in the VCC.
Small capacitors for frequency filtering.

## Slide 14
BW Filter
Ideal capacitor frequency response
Capacitor frequency response due to self inductance
Overlapping impedance curves
Broadband impedance lowered
!
Filtered out

## Slide 15
MOSFET Driver Full Circuit
VCC
In
Out
Ground
Heat sink

## Slide 16
Performance
Higher frequencies does not go through the antenna.
 possible to calculate R  agrees with the max current.

## Slide 17
Performance
With a 1ms pulse @12.8MHz we were able to have a ~35% conversion of atoms into molecules (same efficiency as the 38ms pulse in the PRL 95, 190404 (2005) ).
The molecules are still in the trap!
With a 2ms pulse we get 50% conversion (upper bound for our system’s density)

## Slide 18
Second Order Effects
The total magnetic field applied:
Where is the DC magnetic field.
changes the scattering length and therefor sets the point in which we work.
An RF photon stimulates the atoms to form dimers.

## Slide 19
Second Order Effects
The modulation changes “moves” the scattering length working point.
Since the energy goes like there is a shift to the DC magnetic field in which we see resonance.

## Slide 20
Second Order Effects
The dimer energy depends on the scattering length
This causes a shift in resonance DC magnetic field
The scattering length depends on the magnetic field

## Slide 21
Second Order Effects
We measured a shift of which is equivalent to .
That’s 3 times our temperature!
Strongly modulated regime.
@ 4.6MHz

## Slide 22
Conclusions
We’ve established to produce magnetic field RF pulses with:
  Short pulse time.
  High modulation amplitude – significant affect observed.
  Elegant and simple solution.
This is a super efficient method for experiments that require high current passing through an inductor at high frequencies.

## Slide 23
Registration at http://quest.biu.ac.il/quest2/
Best poster prize!